## Slide 1: Module 4 Wireless Personal Area Networks and Ad hoc Networks
IEEE 802.15.1 (Bluetooth) – Piconet, Scatter net, Protocol Stack; IEEE 802.15.4 (ZigBee) – LRWPAN Device Architecture, Protocol Stack;
Wireless Sensor Network – Design Considerations, Issues and Challenges, WSN Architecture, Applications; Introduction of Ad hoc Networks – MANET and VANET – Characteristics, Applications, Advantages and Limitations; Over view of E-VANET( Electrical Vehicular AdHoc Networks).
Self-learning Topics:- HR–WPAN (UWB)

## Slide 2
Wireless Personal Area Network
Bluetooth
2

## Slide 3
In a WPAN, the residence is connected to a public switched telephone network (PSTN) for telephone services, Internet for web access, and cable network for multichannel television services
Bluetooth enables users to connect a wide range of computing and telecommunication devices without any additional or proprietary cables.
Ultrawide band (UWB-IEEE 802.15.3a) is the IEEE standard for a high-data-rate WPAN designed to provide sufficient quality of service for real-time distribution of content such as video and music.
It is ideally suited for a home multimedia wireless network.
3
Introduction

## Slide 4
The Bluetooth wireless specification includes RF, link layer, and application layer definitions for product developers for data, voice, and content-centric applications.
The specification contains the information necessary to ensure that diverse devices supporting Bluetooth wireless technology can communicate with each other worldwide.
4

## Slide 5
TABLE19.1
5

## Slide 6
Within the home, computers and printers are connected to the Internet through voice band modems, XDSL services, or cable modems.
The industry has two distinct segments—home access and home distribution.
Home access technology uses different wireless and wired alternatives to secure a broadband Internet access to the home gateway to be distributed to the user’s information appliances.
The home distribution or WPAN interconnects all home appliances and connects them to the Internet through a home gateway.
6
The Wireless Personal Area Network

## Slide 7
The WPAN provides an infrastructure to interconnect a variety of home appliances and enables them to access the Internet through a central home gateway.
Home computing equipment used for computing and Internet transaction interface access includes PCs, laptops, printers, scanners, and web cameras.
A home computing network allows multiple computers as well as multiple devices to connect with a network protocol.
7
The Wireless Personal Area Network

## Slide 8
A wireless personal area network (WPAN) is a short-distance (typically 10 m but as far as 20 m) wireless network specially designed to support portable and mobile computing devices such as PCs, PDAs, printers, storage devices, cellphones, pagers, set-up boxes, and a variety of consumer electronic equipment.
Bluetooth (IEEE 802.15.1), UWB (IEEE 802.15.3a), and ZigBee (IEEE 802.15.4) are examples of WPANs that allow devices within close proximity to join together in wireless networks in order to exchange information.
8
The Wireless Personal Area Network

## Slide 9
WPANs such as Bluetooth provide enough bandwidth and convenience to make data exchange practical for certain mobile devices requiring data exchanges at rates up to 1 Mbps.
At the other end of the scale, UWB will provide the capability of streaming video signals at data rates up to 1 Gbps.
Many control and command applications require much lower data rates and also the lowest possible cost, thus ZigBee (250kbps).
9
The Wireless Personal Area Network

## Slide 10
The IEEE 802.15 committee has the responsibility for developing standards for short distance wireless networks used in the networking of portable and mobile computing devices.
IEEE 802.15.1 and 802.15.4 focus on the following characteristics:
Power management: Low current consumption
Range: 0–10 m
Rate: 19.2–1000 kbps
Size: 0.5 in³ without antenna
Low cost relative to target device
Should allow overlap of multiple networks in the same area
Network supports a minimum of 16 devices
10
The Wireless Personal Area Network

## Slide 11
In 1994, the Swedish telecommunication company, Ericsson, decided to honour old, weird Herald I. Bluetooth, king of Denmark between 940 and 985 AD, by naming its new wireless networking standard after him
Bluetooth provides short-range, low-cost connectivity between portable devices.
The low power consumption makes Bluetooth ideal for small, battery-powered devices like mobile phones and pocket PCs.
Bluetooth is limited in range (10 meters) and bandwidth 780 kbps compared to Home RF that goes to 1–2 Mbps and IEEE 802.11b that goes to 11 Mbps with 150 m and greater distance.
11
Bluetooth (IEEE 802.15.1)

## Slide 12
The Bluetooth system operates in the 2.4 GHz Industrial Scientific Medicine (ISM) band.
In a vast majority of countries around the world the range of this frequency band is 2.4–2.4835 GHz.
The ISM band is open to any radio system such as cordless phones, garage door openers, and microwaves, and therefore is susceptible to strong interferences
12
Bluetooth (IEEE 802.15.1)

## Slide 13
Some other features
A Bluetooth WPAN involves up to eight devices, located within a 10-m radius personal operating space, that unite to exchange information or share services.
"ad hoc networking”- Because it can be done spontaneously according to immediate need.
"point-to-point network” -Because a WPAN involves directly networking between different points, without the use of network infrastructure.
absolutely anywhere- at least two Bluetooth devices share a 10-m range.
13
Bluetooth (IEEE 802.15.1)

## Slide 14
fast acknowledgment and frequency hopping scheme - make the link robust.
hops faster and uses shorter packets- Short packets and fast hopping limit the impact of interference from other radio systems that use the same frequency band.
forward error correction (FEC) scheme- limits the impact of random noise on long-distance links.
14
Bluetooth (IEEE 802.15.1)

## Slide 15
Uses of Bluetooth
Bluetooth is being used in mobile computers, bar code laser scanners, cash registers, vending machines, GPS receivers, slide projectors, printers, digital cameras, digital camcorders, test and measurement equipment, and LAN access points.
IEEE 802.15.1. standards development for Bluetooth
The IEEE is also exploring the enhancement of 802.15.1 with a high data rate Bluetooth standard: 802.15.3
15
Bluetooth (IEEE 802.15.1)

## Slide 16
16

## Slide 17
Transmitter equipment is classified into three power classes.
A power control is required for power class 1 equipment, whereas power controls for power class 2 and 3 equipment is optional.
17
Bluetooth (IEEE 802.15.1)

## Slide 19
Bluetooth Architecture

## Slide 20
Piconet: A collection of devices connected via Bluetooth technology in an ad hoc fashion
A piconet starts with two connected devices, such as a PC and cellular phone, and may grow to eight connected devices.( Why maximum 8 devices?
All Bluetooth devices are peer units and have identical implementations.
In a piconet, one unit will act as a master for synchronization purposes, and the other(s) as slave(s) for the duration of the piconet connection.
20
Definitions of the Terms Used in Bluetooth

## Slide 21
Scatternet: Two or more independent and non-synchronized piconets that communicate with each other.
A slave as well as a master unit in one piconet can establish this connection by becoming a slave in the other piconet.
Master unit. The device in the piconet whose clock and hopping sequence are used to synchronize all other devices in the piconet.
Slave units. All devices in a piconet that are not the master (up to seven active units for each master).
21
Definitions of the Terms Used in Bluetooth

## Slide 22
MAC address: A 3-bit medium access control address used to distinguish between units participating in the piconet
Parked units: Devices in a piconet which are time-synchronized but do not have MAC addresses.
Sniff and hold mode: Devices that are synchronized to a piconet, and which have temporarily entered power-saving mode in which device activity is reduced.
22
Definitions of the Terms Used in Bluetooth

## Slide 23
The Bluetooth protocol stack allows devices to locate, connect, and exchange data with each other and to execute interoperable, interactive applications against each other.
The Bluetooth protocol stack can be placed into three groups:
Transport protocol group,
Middleware protocol group,
Application group
23
Bluetooth Protocol Stack
Draw and explain Bluetooth protocol stack

## Slide 24
Fig19.2
24
Logical link control and adaptation protocol
Link manager Protocol

## Slide 26
26
The protocols in this group are designed to allow Bluetooth devices to locate and connect to each other.
These protocols carry audio and data traffic between devices and support both synchronous and asynchronous transmission for telephony-grade voice communication.
Audio traffic is treated with high priority in Bluetooth.
Audio traffic bypasses all protocol layers and goes directly to the baseband layer which then transmits it in small packets directly over Bluetooth’s air interface.
Transport Protocol Group

## Slide 27
27
The protocols in this group are also responsible for managing the physical and logical links between the devices so that the layers above and applications can pass data through the connections.
The protocols in this group are
radio,
baseband,
link manager,
logical link control and adaptation, and
host controller interface (HCI).
Transport Protocol Group

## Slide 28
28
Logical link control and adaptation protocol (L2CAP) layer:
All data traffic is routed through L2CAP layer
This layer shields the higher layers from the details of the lower layers.
It is also responsible for segmenting larger packets from higher layers into smaller packets, which are easier to handle by the lower layer.
The L2CAP layer is responsible for admission control based on the requested level of service and for coordinating with the lower layers to maintain this level of service.
Transport Protocol Group

## Slide 29
29
Link manager Protocol(LMP):
The link manager layers are responsible for negotiating the properties of the Bluetooth air interface between them.
These properties may be anything from bandwidth allocation to support services of a particular type to periodic bandwidth reservation for audio traffic.
This layer is responsible for supervising device pairing.
Device pairing is the creation of a trust relationship between the devices by generating and storing an authentication key for future device authentication.
The link managers are also responsible for power control and may request adjustments in power levels.
Transport Protocol Group

## Slide 30
30
Baseband and radio layers:
The baseband layer is responsible for the process of searching for other devices and establishing a connection with them.
It is also responsible for assigning the master and slave roles.
This layer also controls the Bluetooth unit’s synchronization and transmission frequency hopping sequence.
Transport Protocol Group

## Slide 31
31
Host controller interface (HCI) layer:
The HCI allows higher layers of the stack, including applications, to access the baseband, link manager, etc., through a single standard interface.
Through HCI commands, the module may enter certain modes of operation
Transport Protocol Group

## Slide 32
Middleware Protocol Group
This group comprises the protocols needed for existing applications to operate over Bluetooth links.
The protocols in this group can be third party and industry standard protocols and protocols developed specifically by the Special Interest Group (SIG) for Bluetooth wireless communication.
The protocols in this group can include TCP, IP, PPP, A serial port emulator protocol RFCOMM, service discovery protocol (SDP), etc.,

## Slide 33
RFCOMM layer:
Bluetooth’s prime aim is to eliminate cables and provide support for serial communication without cables.
RFCOMM provides a virtual serial port to applications.
The advantage provided by this layer is that it is easy for applications designed for cabled serial ports to migrate to Bluetooth.
The applications can use RFCOMM much like a serial port to accomplish scenarios like dial-up networking, etc.
RFCOMM is an important part of the protocol stack because of the function it performs.

## Slide 34
Service discovery protocol (SDP) layer:
In Bluetooth wireless communications any two devices can start communicating on the spur of the moment. Once a connection is established there is a need for the devices to find and understand the services the other devices have to offer. This is taken care of in this layer.
The SDP is a standard method for Bluetooth devices to discover and learn about the services offered by the other device.
Service discovery is important in providing value to the end-user.

## Slide 35
Object exchange (OBEX) protocol.
IrOBEX (in short, OBEX) is a session protocol developed by the Infrared Data Association to exchange objects in a simple and spontaneous manner.
OBEX provides the same basic functionality as HTTP but in a much lighter fashion.
It uses a client-server model and is independent of the transport mechanism and transport application programming interface (API), provided it realizes a reliable transport base.

## Slide 36
Networking layers:
Bluetooth wireless communication uses a peer-to-peer network topology rather than an LAN type topology.
Dial-up networking uses the attention (AT) command layer.
In most cases the network that is being accessed is an IP network. Once a dial-up connection is established to an IP network, then standard protocols like TCP, UDP, and HTTP can be used.
A device can also connect to an IP network using a network access point. The Internet PPP is used to connect to the access point.
The specification does not define a profile that uses the TCP/IP directly over Bluetooth links.

## Slide 37
Telephone control specification (TCS) layer and audio:
This layer is designed to support telephony functions, which include call control and group management. These are associated with setting up voice calls.
Once a call is established a Bluetooth audio channel can carry the call’s voice content. TCS can also be used to set up data calls.
The TCS protocols are compatible with ITU specifications.
The SIG is also considered a second protocol called TCS-AT, which is a modem control protocol.

## Slide 38
Audio and Data transmission in Bluetooth
Audio traffic is treated separately in Bluetooth.
Audio traffic is isochronous ( occupying equal time), meaning that it has a time element associated with it.
Audio traffic is routed directly to the baseband.
Special packets called synchronous connection-oriented are used for audio traffic.
Bluetooth audio communication takes place at a rate of 64 kbps using one of the two data encoding schemes —
8-bit logarithmic pulse code modulation
continuos variable slope delta modulation.

## Slide 39
Application Group
This group consists of actual applications that make use of Bluetooth links and refers to the software that exists above the protocol stack.
The software uses the protocol stack to provide some function to the user of the Bluetooth devices.
The Bluetooth-SIG does not define any application protocols nor does it specify any API.
Bluetooth profiles are developed to establish a base point for use of a protocol stack to accomplish a given usage case.

## Slide 40
The Bluetooth baseband technology supports two link types:
Synchronous connection oriented (SCO) type
used primarily for voice
Asynchronous connectionless (ACL) type
used primarily for packet data
Different master-slave pairs of the same piconet can use different link types and the link type may change arbitrarily during a session.
Bluetooth Link Types
Explain Bluetooth link types

## Slide 41
Features
Each link type supports up to sixteen different packet types.
Four of these are control packets and are common for both SCO and ACL links.
Both link types use a time division duplex (TDD) scheme for full-duplex transmission.
The SCO link is symmetric and typically supports time-bounded voice traffic.
SCO packets are transmitted over reserved intervals.
Once the connection is established, both master and slave units may send SCO packets without being polled.
The SCO link type supports and is used often for voice traffic.
The data circuit-switched, point-to-point connections for SCO links is 64 kbps.

## Slide 42
The ACL link is packet oriented and supports both symmetric and asymmetric traffic.
The master unit controls the link bandwidth and decides how much piconet bandwidth is given to each slave, and the symmetry of the traffic.
Slaves must be polled before they can transmit data.
The ACL link also supports broadcast messages from the master to all slaves in the piconet.
Multislot packets can be used in ACL and they can reach maximum data rates of 721 kbps in one direction and 57.6 kbps in the other direction if no error correction is used
Features

## Slide 43
Data packets are protected by an automatic retransmission query (ARQ) scheme.
Thus, when a packet arrives, a check is performed on it.
If there is an error detected, the receiving unit indicates this in the return packet.
In this way, retransmission is done only for the faulty packets. Retransmission is not feasible for voice so better error protection is used.

## Slide 47
A symmetric 1-slot DH1 link between the master and slave carries 216 bits per slot at a rate of 800 slots per second in each direction. The associated rate is 216 X 800 =172.8 kbps.
The asymmetric DM5 link uses a 5-slot packet carrying 1792 bits per packet by the master and a 1-slot packet carrying 136 bits per packet by the slave terminal.
The number of packets per second in each direction is 1600/6. ( 1600 hopping rate per second).
The data rate of the master is 1792 X 1600/6 = 477.8 kbps and the data rate of the slave terminal is 136 X 1600/6 = 36.3 kbps.

## Slide 48
The asymmetric DH5 link uses a 5-slot packet carrying 2712 bits per packet by the master and a 1-slot packet carrying 216 bits per packet by the slave terminal.
The number of packets in each direction is 1600/6 packets per second.
The data rate of the master is 2712 X 1600/6 = 723.2 kbps and the data rate of the slave terminal is 216 X 1600/6 = 57.6 kbps.

## Slide 49
ZigBee Technology

## Slide 50
Low rate (LR) wireless personal access network (WPAN) (IEEE 802.15.4/LRWPAN)
is intended to serve a set of industrial, residential, and medical applications.
very low power consumption, low cost requirement, and relaxed needs for data rate and QoS.
The low data rate enables the LR-WPAN to consume little power.
ZigBee technology is a low data rate, low power consumption, low cost, wireless networking protocol targeted toward automation and remote control applications.
Introduction

## Slide 51
The IEEE 802.15.4 committee and ZigBee Alliance worked together and developed the technology commercially known as ZigBee.
Features/ characteristics:
1) ZigBee-compliant wireless devices are expected to transmit 10–75 minutes, depending on the RF environment and power output consumption required for a given application.
2) Operate in the unlicensed RF worldwide (2.4 GHz global, 915 MHz America, or 868 MHz Europe) bands.
3) The data rate is
250 kbps at 2.4 GHz,
40 kbps at 915 MHz, and
20 kbps at 868 MHz.

## Slide 52
The IEEE 802.15.4 committee is focusing on the specifications of the lower two layers of the protocol (the physical and data link layers).
On the other hand, ZigBee Alliance aims to provide the upper layers of the protocol stack (from the network to the application layer) for interoperable data interworking, security services, and a range of wireless home and building control solutions.
ZigBee often uses a basic master-slave configuration suited to static star networks of many infrequently used devices that talk via small data packets. It allows up to 254 nodes.
Other network topologies such as peer-to-peer and cluster tree are also used.

## Slide 53
ZigBee Components and Network Topologies
Device- A device can be a full-function device (FFD) or reduced-function device (RFD).
A network includes at least one FFD, operating as the personal area network (PAN) coordinator.
The FFD can operate in three modes:
a PAN coordinator,
a coordinator,
or a device.
An RFD is intended for applications that are extremely simple and do not need to send large amounts of data.
An FFD can talk to reduced-function or full-function devices, while an RFD can only talk to an FFD.

## Slide 54
ZigBee supports three types of topologies:
star topology,
peer-to-peer topology
cluster tree
In the star topology, communication is established between devices and a single central controller, called the PAN coordinator.
The PAN coordinator may be powered by mains while the devices will most likely be battery powered.

## Slide 55
Applications that benefit from this topology are
home automation,
personal computer (PC) peripherals,
toys, and games.
After an FFD is activated for the first time, it may establish its own network and become the PAN coordinator.
Each star network chooses a PAN identifier, which is not currently used by any other network within the radio sphere of influence.
This allows each star network to operate independently.

## Slide 56
In the peer-to-peer topology, there is also one PAN coordinator.
In contrast to star topology, any device can communicate with any other device as long as they are in range of one another.
A peer-to-peer network can be ad hoc, self-organizing, and self-healing.
Applications such as
industrial control and monitoring,
wireless sensor networks and
asset and inventory tracking would benefit from such a topology.
It also allows multiple hops to route messages from any device to any other device in the network.
It can provide reliability by multipath routing.

## Slide 57
The cluster-tree topology is a special case of a peer-to-peer network in which most devices are full-function devices and an RFD may connect to a cluster-tree network as a leaf node at the end of a branch.
Any of the full-function devices can act as a coordinator and provide synchronization services to other devices and coordinators.
However, only one of these coordinators is the PAN coordinator.
The PAN coordinator forms the first cluster by establishing itself as the cluster head (CLH) with a cluster identifier (CID) of zero, choosing an unused PAN identifier, and broadcasting beacon frames to neighboring devices.

## Slide 58
A candidate device receiving a beacon frame may request to join the network at the cluster head. If the PAN coordinator permits the device to join, it will add this new device to its neighbor list.
The newly joined device will add the cluster head as its parent in its neighbor list and begin transmitting periodic beacons such that other candidate devices may then join the network at that device.
Once application or network requirements are met, the PAN coordinator may instruct a device to become the cluster head of a new cluster adjacent to the first one.
The advantage of the clustered structure is the increased coverage at the cost of increased message latency. (Explain Zigbee topologies)

## Slide 59
IEEE 802.15.4 LR-WPAN Device Architecture
The device comprises a physical layer (PHY), which contains the RF transceiver along with its low-level control mechanism.
A MAC sublayer provides access to the physical channel for all types of transfer.
The upper layers consist of a network layer, which provides network configuration, manipulation, and message routing, and an application layer, which provides the intended function of a device.
An IEEE 802.2 logical link control (LLC) can access the MAC through the service specific convergence sublayer (SSCS).

## Slide 60
Physical Layer
The PHY (IEEE 802.15.4) provides two services:
The PHY data service and
The PHY management service interfacing to the physical layer management entity (PLME).
The PHY data service enables the transmission and reception of PHY protocol data units (PPDUs) across the physical radio channel.
The features of the PHY are activation and deactivation of the radio transceiver, energy detection (ED), link quality indication (LQI), channel selection, clear channel assessment (CCA) and transmitting as well as receiving packets across the physical medium.

## Slide 61
The standard provides two options based on the frequency band. Both are based on direct sequence spread spectrum (DSSS).
The data rate is 250 kbps at 2.4 GHz, 40 kbps at 915 MHz, and 20 kbps at 868 MHz.
The higher rate at 2.4 GHz is attributed to a higher-order modulation scheme.
Lower frequency provides longer range due to lower propagation losses. Low rate can be translated into better sensitivity and larger coverage area.
Higher rate means higher throughput, lower latency, or lower duty cycle.

## Slide 63
To maintain a common simple interface with MAC, both PHY share a single packet structure (see Figure 20.7).
Each PHY protocol data units PPDU contains a
synchronization header (preamble plus start of packet delimiter),
a PHY header to indicate the packet length, and
the payload, or PHY service data unit (PSDU).
The 32-bit preamble is designed for the acquisition of symbol and chip timing, and in some cases may be used for coarse frequency adjustment.
Channel equalization is not required for either PHY due to the combination of small coverage area and relatively low chip rates.

## Slide 64
Within the PHY header, 8 bits are used to specify the length of the payload (in bytes). This supports packets of length 0–127 bytes, although, due to MAC layer overhead, zero-length packets will not occur in practice.

## Slide 65
Typical packet sizes for home applications such as monitoring and control security, lighting, air conditioning, and other appliances are expected to be of the order of 30–60 bytes,
while more demanding applications such as interactive games and computer peripherals, or multihop applications with more address overhead, may require larger packet sizes.
Adjusting transmission rates in each frequency band, the maximum packet durations are
4.25 ms for the 2.4 GHz band,
26.6 ms for the 915 MHz band, and
53.2 ms for the 868 MHz band.

## Slide 66
The 868/915 MHz PHY uses a simple DSSS approach in which each transmitted bit is represented by a 15-chip maximum length sequence.
Binary data is encoded by multiplying each m-sequence by 1 or -1, and the resulting chip sequence is modulated onto the carrier using binary phase shift keying (BPSK).
Differential data encoding is used prior to modulation to allow low-complexity differential coherent reception.
868/915 MHz PHY features

## Slide 67
The 2.4 GHz PHY uses a 16-ary quasi-orthogonal modulation technique based on DSSS methods.
Binary data is grouped into 4-bit symbols, and each symbol specifies one of sixteen nearly orthogonal 32-chip, pseudo-random noise (PN) sequences for transmission.
PN sequences for successive data symbols are concatenated, and the aggregate chip sequence is modulated onto the carrier using, offset-quadrature phase shift keying (OQPSK).
2.4 GHz PHY features

## Slide 68
Data Link Layer
The data link layer (IEEE 802.15.4) is divided into two sublayers, the MAC and LLC sublayers.
The logical link control is standardized in IEEE 802.2 and is common among all IEEE 802 standards.
The IEEE 802.15.4 MAC provides services to an IEEE 802.2 type logical link control through the service-specific convergence sublayer (SCCS), or a proprietary LLC can access the MAC services directly without going through the SCCS.
The SCCS ensures compatibility between different LLC sublayers and allows the MAC to be accessed through a single set of access points.

## Slide 69
The features of the IEEE 802.15.4 MAC are
association and disassociation,
acknowledged frame delivery,
channel access mechanism,
frame validation,
guaranteed time slot management,
beacon management.

## Slide 70
The MAC provides two services to higher layers that can be accessed through two service access points (SAPs).
The MAC data service is accessed through the MAC common part sublayer (MCPS-SAP),
The MAC management services are accessed through the MAC layer management entity (MLME-SAP).
These two services provide an interface between the SCCS or another LLC and the physical layer accommodate the needs of different applications and network topologies while maintaining a simple protocol.

## Slide 72
The MAC protocol data unit (MPDU) consists of the
MAC header (MHR),
MAC service data unit (MSDU), and
MAC footer (MFR).
MAC header
Frame control field-indicates the type of MAC frame being transmitted,
specifies the format of the address field, and
controls the acknowledgment.
The frame control field specifies how the rest of the frame looks and what it contains.
Address field: The size of the address field may vary between 0 and 20 bytes.
The flexible structure of the address field helps to increase the efficiency of the protocol by keeping the packet shorts.

## Slide 73
The payload field is variable in length; however, the complete MAC frame may not exceed 127 bytes in length. The data contained in the payload is dependent on the frame type.
The IEEE 802.15.4 MAC has four different frame types.
Beacon frame,
Data frame,
Acknowledgment frame
MAC command frame
Only the data and beacon frames actually contain information sent by higher layers; the acknowledgment and MAC command frames originate in the MAC and are used for MAC peer-to-peer communication.
Payload field

## Slide 74
Superframe Structure
Some applications may require a dedicated bandwidth to achieve low latencies. To accomplish these low latencies, the IEEE 802.15.4 LR-WPAN can operate in an optional superframe mode.
In a superframe (see Figure 20.9), a dedicated PAN coordinator transmits superframe beacons in predetermined intervals.
These intervals can be as short as 15 ms or as long as 245 seconds.
The time between two beacons is divided into 16 equal time slots independent of the duration of the superframe.
The beacon frame is sent in the first slot of each superframe.

## Slide 75
The beacons are used to synchronize the attached devices, to identify PAN, and describe the structure of superframes.
A device can transmit at any time during the slot, but must complete its transaction before the next superframe beacon.

## Slide 76
The channel access in time slots is contention based;
however, the PAN coordinator may assign time slots to a single device that requires a dedicated bandwidth or low latency transmissions.
These assigned time slots are called guaranteed time slots (GTSs)
It form a contention-free period (CFP) located immediately before the next beacon.

## Slide 77
The size of the CFP may vary depending on the demand by the associated network devices;
when guaranteed time slots are used, all devices must complete their contention-based transactions before the CFP begins.
The beginning of the CFP and duration of the superframe are communicated to the attached network devices by the PAN coordinator.
The PAN coordinator may allocate up to 7 of the GTSs and a GTS can occupy more than one slot period.

## Slide 78
The network layer of Zigbee (IEEE 802.15.4) is responsible for topology construction and maintenance as well as naming and binding services, which include the tasks of addressing, routing, and security.
The network layer should be self organizing and self-maintaining to minimize energy consumption and total cost.
IEEE 802.15.4 supports multiple network topologies, including star, peer-to-peer, and cluster tree .The topology is an application design choice
The Network Layer

## Slide 79
Routing Protocol
Routing protocols for ad hoc networks can be divided into two groups: table-driven (proactive) and source-initiated on-demand-driven (reactive)
The table-driven approach has low latency and high overhead, and is more suitable when time constraints are significant.
The source-initiated on-demand-driven approach has high latency and low overhead.

## Slide 80
It is more suitable for a mobile environment with a limited bandwidth capacity.
The table-driven routing protocols attempt to maintain consistent, up-to-date routing information from each node to every node in the network.
These protocols require each node to maintain one or more tables to store routing information,
The Destination Sequenced Distance Vector (DSDV), Wireless Routing Protocol (WRP), and Cluster Switch Gateway Routing (CSGR) protocol belong to this category
Table-driven (proactive)

## Slide 81
The source-initiated on-demand-driven routing protocols create routes only when desired by a source node.
When a node requires a route to a destination, it initiates a route discovery process within the network.
This process is completed once a route is found or all possible route permutations have been examined.
source-initiated on-demand-driven (reactive)

## Slide 82
The Ad hoc On-demand Distance Vector (AODV), Dynamic Source Routing (DSR), Temporally Ordered routing algorithm (TORA), and Cluster Based Routing Protocol (CBRP) belong to this category
The AODV is a pure on-demand route acquisition algorithm in which nodes that do not lie on active paths neither maintain nor participate in any periodic routing table exchanges
The primary objectives of the algorithm are to broadcast discovery packets only when necessary

## Slide 83
Application Layer:
There are two profiles at this layer.
Manufacturer specific application profile- Operate as closed systems and also ensure that they can coexist with other zigbee systems.
Public application profile- for this to work interoperability between various zigbee devices is a must.
A single zigbee node supports up to 240 application objects called end points.
An end point specifies specific application, for example, 0 dedicated to ZDO (Zigbee device object), provides control and management commands.
6 used for control of light. 8 used for managing heating and air conditioning.

## Slide 84
The ZigBee APL layer consists of three sections, shown in below Figure.
the application support (APS) sublayer, ZigBee Device Objects (ZDO), and the application framework. The application support sublayer (APS) provides an interface between the network layer (NWK) and the application layer (APL).
APS (AF) | Application layer that defines various addressing objects including profiles, clusters, and endpoints.
ZDO | Application layer that provides device and service discovery features and advanced network management capabilities.

## Slide 85
WSN Wireless sensor Network)

## Slide 86
What is WSN?
The WSN (Wireless Sensor Network) consists of end sensor nodes, routing nodes and base station or data collector sink node (or base station or gateway). The WSN should be scalable and secure to deliver efficient and reliable network.
The WSN can be classified based on network type, clustering, communication method, protocol, application usage and coverage.

## Slide 87
WSN consists of spatially distributed autonomous sensing devices used to monitor physical or environmental conditions such as temperature, pressure, sound, vibration, motion or pollutants at different locations.
All the nodes communicate wirelessly in WSN and follows various routing protocols.
WSN operates in bandwidth and performance constrained environment. WSNs are self organizing multi-hop ad hoc networks.

## Slide 88: Characteristics of Wireless Sensor Networks
Wireless Sensor Networks mainly consists of sensors. Sensors are -
  low power
  limited memory
  energy constrained due to their small size.
Wireless networks can also be deployed in extreme environmental conditions and may be prone to enemy attacks.
Although deployed in an ad hoc manner they need to be self organized and self healing and can face constant reconfiguration.

## Slide 89
Some of the characteristic features of sensor networks include the following
  Sensor nodes are densely deployed.
  Sensor nodes are prone to failures.
  The topology of a sensor network changes very frequently.
  Sensor nodes are limited in power, computational capacities, and
  memory.
  Sensor nodes may not have global identification because of the
  large amount of overhead and the large number of sensors.

## Slide 90
Benefits or advantages of WSN
Following are the benefits or advantages of WSN: ➨It is scalable and hence can accommodate any new nodes or devices at any time. ➨It is flexible and hence open to physical partitions. ➨All the WSN nodes can be accessed through centralized montoring system. ➨As it is wireless in nature, it does not require wires or cables. Refer difference between wired network vs wireless network ➨WSNs can be applied on large scale and in various domains such as mines, healthcare, surveillance, agriculture etc. ➨It uses different security algorithms as per underlying wireless technologies and hence provide reliable network for consumers or users.

## Slide 91
Drawbacks or disadvantages of WSN
Following are the drawbacks or disadvantages of WSN:
➨As it is wireless in nature, it is prone to hacking by hackers. ➨It can not be used for high speed communication as it is designed for low speed applications. ➨It is expensive to build such network and hence can not be affordable by all. ➨There are various challenges to be considered in WSN such as energy efficiency, limited bandwidth, node costs, deployment model, Software/hardware design constraints and so on. ➨In star topology based WSN, failure of central node leads to whole network shutdown.

## Slide 92: Challenges in WSN
A modern Wireless Sensor Network (WSN) faces several challenges, including:
Limited power and energy: WSNs are typically composed of battery-powered sensors that have limited energy resources. This makes it challenging to ensure that the network can function for long periods of time without the need for frequent battery replacements.
Limited processing and storage capabilities: Sensor nodes in a WSN are typically small and have limited processing and storage capabilities. This makes it difficult to perform complex tasks or store large amounts of data.
Heterogeneity: WSNs often consist of a variety of different sensor types and nodes with different capabilities. This makes it challenging to ensure that the network can function effectively and efficiently.
Security: WSNs are vulnerable to various types of attacks, such as eavesdropping, jamming, and spoofing. Ensuring the security of the network and the data it collects is a major challenge.

## Slide 93
Scalability: WSNs often need to be able to support a large number of sensor nodes and handle large amounts of data. Ensuring that the network can scale to meet these demands is a significant challenge.
Interference: WSNs are often deployed in environments where there is a lot of interference from other wireless devices. This can make it difficult to ensure reliable communication between sensor nodes.
Reliability: WSNs are often used in critical applications, such as monitoring the environment or controlling industrial processes. Ensuring that the network is reliable and able to function correctly in all conditions is a major challenge.

## Slide 94: Challenges in sensor networks
Energy constraint
Unreliable communication
Unreliable sensors
Ad hoc deployment
Large scale networks
Limited computation power
Distributed execution
Nodes are battery powered
Radio broadcast, limited bandwidth, bursty traffic
False positives
Pre-configuration inapplicable
Algorithms should scale well
Centralized algorithms inapplicable
Difficult to debug & get it right

## Slide 97
The following are important issues pertaining to WSNs:
sensor type;
sensor placement;
sensor power consumption,
operating environment,
capabilities and signal processing,
connectivity, and telemetry or control of remote devices.
It is critical to note that node location and fine-grained time (stamping) are essential for proper operation of a sensor network.

## Slide 98
Types of Wireless Sensor Networks

## Slide 100
Typical sensor network arrangement

## Slide 101
Sensor networks require sensing systems that are long-lived and environmentally resilient.
Unattended, untethered, self-powered low-duty-cycle systems are typical.
In most instances, communication circuitry and antennas are the primary elements that draw most of the energy.
Sensors are either passive or active devices. Passive sensors in element form include seismic-, acoustic-, strain-, humidity-, and temperature-measuring devices.
Passive sensors tend to be low-energy devices.
Active sensors include radar and sonar; these tend to be high-energy systems

## Slide 103
Components of WSN:
Sensor node: Sensors in WSN are used to capture the environmental variables and which is used for data acquisition. Sensor signals are converted into electrical signals.
Radio Nodes: It is used to receive the data produced by the Sensors and sends it to the WLAN access point. It consists of a microcontroller, transceiver, external memory, and power source.
WLAN Access Point: It receives the data which is sent by the Radio nodes wirelessly, generally through the internet.
Evaluation Software: The data received by the WLAN Access Point is processed by a software called as Evaluation Software for presenting the report to the users for further processing of the data which can be used for processing, analysis, storage, and mining of the data.

## Slide 106: Applications of Wireless Sensor networks
The applications can be divided in three categories:
Monitoring of objects.
Monitoring of an area.
Monitoring of both area and objects.
* Classification due to Culler, Estrin, Srivastava

## Slide 107: Monitoring Area
Environmental and Habitat Monitoring
Precision Agriculture
Indoor Climate Control
Military Surveillance
Treaty Verification
Intelligent Alarms

## Slide 108: Example: Precision Agriculture
Precision agriculture aims at making cultural operations more efficient, while reducing environmental impact.
The information collected from sensors is used to evaluate optimum sowing density, estimate fertilizers and other inputs needs, and to more accurately predict crop yields.
Notes: Ref-http://www.agrisupportonline.com/phy/index.htm

## Slide 109: Monitoring Objects
Structural Monitoring
Eco-physiology
Condition-based Maintenance
Medical Diagnostics
Urban terrain mapping

## Slide 110: Example: Condition-based Maintenance
Intel fabrication plants
  Sensors collect vibration data, monitor wear and tear; report data in real-time
  Reduces need for a team of engineers; cutting costs by several orders of magnitude

## Slide 111: Monitoring Interactions between Objects and Space
Wildlife Habitats
Disaster Management
Emergency Response
Ubiquitous Computing
Asset Tracking
Health Care
Manufacturing Process Flows

## Slide 112: Example: Habitat Monitoring
The ZebraNet Project
  Collar-mounted sensors monitor zebra movement in Kenya
Source: Margaret Martonosi, Princeton University

## Slide 113: Future of WSN Smart Home / Smart Office
Sensors controlling appliances and electrical devices in the house.
Better lighting and heating in office buildings.
The Pentagon building has used sensors extensively.

## Slide 114: Biomedical / Medical
Health Monitors
  Glucose
  Heart rate
  Cancer detection
Chronic Diseases
  Artificial retina
  Cochlear implants
Hospital Sensors
  Monitor vital signs
  Record anomalies

## Slide 115: Military
Remote deployment of sensors for tactical monitoring of enemy troop movements.

## Slide 116: Industrial & Commercial
Numerous industrial and commercial applications:
  Agricultural Crop Conditions
  Inventory Tracking
  In-Process Parts Tracking
  Automated Problem Reporting
  RFID – Theft Deterrent and Customer Tracing
  Plant Equipment Maintenance Monitoring

## Slide 117: Traffic Management & Monitoring
Future cars could use wireless sensors to:
  Handle Accidents
  Handle Thefts
Sensors embedded in the roads to:
  Monitor traffic flows
  Provide real-time route updates